## Slide 1: Looping Structure
Course Code: COE 3205
Dept. of Computer Science
Faculty of Science and Technology
Lab No: | 8 | Week No: | 9 | Semester: | Spring 21-22
Lecturer: | Noboranjan Dey; noboranjan@aiub.edu |  |  |  | 
Course Title: Computer Organization & Architecture

## Slide 2: Lab Outline
A loop Is a sequence of instructions that is repeated.
The number of times to repeat may be known in advance, or
It may depend on conditions
  FOR LOOP
  WHILE LOOP
  REPEAT LOOP

## Slide 3: FOR LOOP
The control is transferred to destination_label until CX becomes 0.
A FOR LOOP can be implemented using the LOOP instruction:
TOP:
;initialize CX to loop_count
;body of the loop
LOOP TOP

## Slide 4: FOR LOOP-Example
Write a count-controlled loop to display a row of 80 stars:
FOR 80 times DO
display ‘*’
END_FOR
        MOV CX,0
        MOV AH,2
        MOV DL, '*'
TOP:
          INT 21H
          LOOP TOP

## Slide 5: Lab Tasks
Task: 1
Write an assembly probram to print all the ASCII code from 0 to 255. Hints: use jnz and dec instructions
    Sample Output

## Slide 6: Lab Tasks
Task: 2
Put the sum of the first 50 terms of the arithmetic sequence
I, 5, 9, 13, ... in DX. Hints: Employ LOOP instructions to do the following.
    first we find how many loops needed:
    (last term – first term )/ difference
    (148 – 1)/3 = 49 loops
    So put cx = 49

## Slide 7: Lab Tasks
Task: 3
Put the sum 100 + 95 + 90 + ... + 5 in AX. Hints: Employ LOOP instructions to do the following.
    first we find how many loops needed:
    (last term – first term )/ difference
    (100 – 5)/5 = 19 loops
    So put cx = 19

## Slide 8: Lab Tasks
Task: 4
Read a character and display it 50 times on the next line. Hints: use LOOP instructions and put cx = 50
    Sample Output
    Enter a character: d
    Dddddddddddddddddddddddddddddddddddddddddddddddddd
    Thank you.

## Slide 9
Books
Assembly Language Programing and Organization of the IBM PC
Ytha Yu
Charles Marut

## Slide 10
References